## Slide 1: How to Upgrade DWC-BVI2IR
DWC-BVI2IR

## Slide 2: HOW TO UPGRADE VMAXIP’s IP Camera
Disconnect all 4 cameras from VMAX IP™ internal PoE switch.
Connect the 4 Cameras to a PoE switch connected to a DHCP router in order to assign the camera an IP address automatically.
Install “Ipfinderwizard” on PC from the zip file.
Connect the PC you are using for the upgrade to the same PoE switch as the IP cameras.
Run the “Ipfinderwizard” software.

## Slide 3: HOW TO UPGRADE VMAXIP’s IP Camera
Click the ‘Start’ button.
All IP Cameras connected to the PoE switch will be listed.
Click PNC-503H Tab.
Check the camera’s current version.
Select the camera that need to be upgraded
Press Upgrade button.

## Slide 4: HOW TO UPGRADE VMAXIP’s IP Camera
Select the firmware file from the zip folder (*.pk).
Press the ‘Open’ button.
All selected cameras will start the upgrade process automatically
You can track the upgrade process via the progress bar for each camera.

## Slide 5: HOW TO UPGRADE VMAXIP’s IP Camera
Once the upgrade is completed, press the ‘Refresh’ button to search for the cameras
Make sure the new firmware was successfully registered at the camera.
Once all cameras have been upgraded, reconnect them to the VMAX IP™ NVR system.

## Slide 6
Questions?
Thank you!